## Slide 1: Mimic One Frame Build Instruction (Example)

## Slide 2
Extruded 2040 Base
2020 Frame Supports (6)
2020 Vertical Supports (4)
Support Rods with Base (3)
FWD

## Slide 3
Extruded 2040 Base
2020 Frame Supports (6)
Frame Supports attached to 2040 Base by 2 small L-brackets using Button Hex Screws
Step 1: Attach Frame Supports to 2040 Base (6 places)
2 small L-brackets each support, 2 Button Hex Screws each small L-bracket
L-brackets
~610mm
~610mm
Measurements are from centerline to centerline

## Slide 4
Extruded 2040 Base (both grooves)
2020 Frame Supports (6)
Step 1a: Cut Rubber Strips for Frame Supports (6 places) and 2040 Base (both grooves)
Install Rubber Strips in the underside grooves of Frame Supports and 2040 Base.
Rubber Strip
Underside Groove
2040 Base shown upside down
The Rubber Strip provides friction with the table and to fill the space between the table and the Rubber Feet on the end of the Frame Supports.

## Slide 5
Extruded 2040 Base
2020 Frame Supports (6)
Frame Supports attached to 2040 Base by 2 small L-brackets and 1 T-plate using Button Hex Screws
Step 2: Install T-Plates on end Frame Supports in the rear groove of the 2040 (2 places)
1 T-plate per end Frame Support, 5 Button Hex Screws and T-nuts on each T-plate
L-brackets
T-plate

## Slide 6
Extruded 2040 Base
2020 Frame Supports (6)
Step 3: Install T-Plates on center Frame Supports – one in forward groove, one in rear groove (2 places)
1 T-plate per center Frame Support, 5 Button Hex Screws and T-nuts on each T-plate
Forward Groove in 2040
FWD
T-plates
Rear Groove in 2040

## Slide 7
Extruded 2040 Base
Vertical Supports attached to forward groove on 2040 Base by 2 small L-brackets using Button Hex Screws
L-brackets
2020 Vertical Supports (4)
Step 4: Attach Vertical Supports to forward groove in 2040 Base (4 places)
2 small L-brackets each support, 2 Button Hex Screws each small L-bracket
FWD
Vertical Supports (without T-plates) attached to forward groove with 2 small
L-brackets using
Button Hex screws
433mm
347mm
446mm
L-brackets
Measurements are centerline to centerline.
Need to update: outside dimensions should be the same.

## Slide 8
Extruded 2040 Base
2020 Vertical Supports (4)
Step 5: Add 1 large L-bracket anchored in rear groove in 2040 Base on center supports(2 places)
1 large L-bracket each support, 2 Button Hex Screws each small L-bracket
FWD
Vertical Supports (without T-plates) attached to forward groove with 2 small
L-brackets and 1
L-bracket anchored in rear groove

## Slide 9
Extruded 2040 Base
Support Rod Base attached to 2020 Frame Support by 1 large
L-bracket using Button Hex Screws
Support Rods with Base (3)
Step 6: Support Rod Bases on center Frame Supports (3 places)
1 large L-bracket per Support Rod Base, 2 Button Hex Screws each L-bracket
L-brackets
160mm
243mm
2020 Frame Supports (6)
Vertical 2020 is flush
with end of the horizontal 2020

## Slide 10
Extruded 2040 Base
Rubber Feet on Support Rod Base
Support Rods with Base (3)
Step 7: Install Rubber Feet on Support Rod Bases (3 places)
Rubber Feet finish off ends of extruded Support Rod Bases and provide additional support with rods
2020 Frame Supports (6)
Note, a cut will need to be made or a small hole drilled to allow Support Rod to pass through – hole must be smaller than rod to provide friction for extra stability
Add new photo with rubber

## Slide 11
Extruded 2040 Base
Step 8: Insert Support Rods in Support Rod Bases (3 places)
Support Rod will drop down into groove of Frame Support
Support Rods with Base (3)
2020 Frame Supports (6)
Support Rod inserted through Rubber Feet into Support Rod Base
Add new photo with rubber

## Slide 12
Extruded 2040 Base
Support Rods with Base (3)
Step 9: Install Rubber Feet on Frame Supports (6 places)
Rubber Feet finish off ends of Frame Supports and provide friction with table
2020 Frame Supports (6)

## Slide 13
Extruded 2040 Base
End Cap (2) inserted into end of 2040 Base
Step 10: Install End Caps on 2040 Base ends (2 places)
End Caps finish off ends of 2040 Base